Speechpp
05/10/18

In the speechpp.pcf set_io i_clk R9. Pin R9 on the icoboard ICE_CLK is connected to IOB_81_GBIN5 on the right side of the image below.

Post on #yosys
Pin C8 is my USER_CLK comes from a 100MHz osc. It is connected to IOT_197_GBIN1 on HX8K. When I try using it for as an input to PLL I get the fatal error: bad constraint on `i_clk': no PLL at pin C8.
Can only certain pins be used as inputs to PLL?
daveshah
develonepi3: use the SB_PLL40_CORE instead of SB_PLL40_PAD variant (and REFERENCECLK in instead of PACKAGEPIN)
on the left side of the image below.

ICOBOARD RPI

CATBOARD RPI

icepll -i 100 -o 66 -f pll_para.v

F_PLLIN: 100.000 MHz (given)
F_PLLOUT: 66.000 MHz (requested)
F_PLLOUT: 65.972 MHz (achieved)

FEEDBACK: SIMPLE
F_PFD: 11.111 MHz
F_VCO: 1055.556 MHz

DIVR: 8 (4'b1000)
DIVF: 94 (7'b1011110)
DIVQ: 4 (3'b100)

FILTER_RANGE: 1 (3'b001)

PLL configuration written to: pll_para.v

sb_pll40_pad.v
 module top(
input PACKAGEPIN,
output PLLOUTCORE,
output PLLOUTGLOBAL,
input EXTFEEDBACK,
input [7:0] DYNAMICDELAY,
output LOCK,
input BYPASS,
input RESETB,
input LATCHINPUTVALUE,

//Test Pins
output SDO,
input SDI,
input SCLK
);
SB_PLL40_PAD #(
.FEEDBACK_PATH("DELAY"),
// .FEEDBACK_PATH("SIMPLE"),
// .FEEDBACK_PATH("PHASE_AND_DELAY"),
// .FEEDBACK_PATH("EXTERNAL"),

.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
// .DELAY_ADJUSTMENT_MODE_FEEDBACK("DYNAMIC"),

.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
// .DELAY_ADJUSTMENT_MODE_RELATIVE("DYNAMIC"),

.PLLOUT_SELECT("GENCLK"),
// .PLLOUT_SELECT("GENCLK_HALF"),
// .PLLOUT_SELECT("SHIFTREG_90deg"),
// .PLLOUT_SELECT("SHIFTREG_0deg"),

.SHIFTREG_DIV_MODE(1'b0),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0000),
.DIVF(7'b0000000),
.DIVQ(3'b001),
.FILTER_RANGE(3'b000),
.ENABLE_ICEGATE(1'b0),
.TEST_MODE(1'b0)
) uut (
.PACKAGEPIN (PACKAGEPIN ),
.PLLOUTCORE (PLLOUTCORE ),
.PLLOUTGLOBAL (PLLOUTGLOBAL ),
.EXTFEEDBACK (EXTFEEDBACK ),
.DYNAMICDELAY (DYNAMICDELAY ),
.LOCK (LOCK ),
.BYPASS (BYPASS ),
.RESETB (RESETB ),
.LATCHINPUTVALUE(LATCHINPUTVALUE),
.SDO (SDO ),
.SDI (SDI ),
.SCLK (SCLK )
);
endmodule