Speechpp
05/10/18

In the speechpp.pcf set_io i_clk R9. Pin R9 on the icoboard ICE_CLK is connected to IOB_81_GBIN5 on the right side of the image below.

Post on #yosys
Pin C8 is my USER_CLK comes from a 100MHz osc. It is connected to IOT_197_GBIN1 on HX8K. When I try using it for as an input to PLL I get the fatal error: bad constraint on `i_clk': no PLL at pin C8.
Can only certain pins be used as inputs to PLL?
daveshah
develonepi3: use the SB_PLL40_CORE instead of SB_PLL40_PAD variant (and REFERENCECLK in instead of PACKAGEPIN)
on the left side of the image below.

ICOBOARD RPI

CATBOARD RPI

make speechpp
write_txt speechpp.asc...
icetime -d hx8k -c 75 speechpp.asc
// Reading input .asc file..
// Reading 8k chipdb file..
// Creating timing netlist..
// Timing estimate: 10.21 ns (97.91 MHz)
// Checking 13.33 ns (75.00 MHz) clock constraint: PASSED.
icepack speechpp.asc speechpp.bin
rm speechpp.asc

verilator -Wall -I../pport/ --cc speechpp.v
cd obj_dir/
make -f Vspeechpp.mk

R9 on the icoboard ICE_CLK IOB_81_GBIN5 which RPI_ICE_CLK pin 7 GPIO 4 on RPi.
On the catboard BCM4_GPCLK0 IOB_81_GBIN5
netpport.cpp

// RPi GPIO #, connector pin #, schematic name, fpga pin #
//
# define RASPI_D8 0 // PIN 11, GPIO.0, IO219, D5
# define RASPI_D7 1 // PIN 12, GPIO.1, IO212, D6
# define RASPI_D6 3 // PIN 15, GPIO.3, IO209, C6
# define RASPI_D5 4 // PIN 16, GPIO.4, IO206, C7
# define RASPI_D4 12 // PIN 19, MOSI, RPI_SPI_MOSI,A6
# define RASPI_D3 13 // PIN 21, MISO, RPI_SPI_MISO,A7
# define RASPI_D2 11 // PIN 26, CE1, IO224, D4
# define RASPI_D1 24 // PIN 35, GPIO.24, IO210, D7
# define RASPI_D0 27 // PIN 36, GPIO.27, IO193, D9
# define RASPI_DIR 28 // PIN 38, GPIO.28, IO191, C9
# define RASPI_CLK 29 // PIN 40, GPIO.29, IO185, C10
set_io io_pp_data[0] D9	36	R4
set_io io_pp_data[1] D7	35	T3
set_io io_pp_data[2] D4	26	T7
set_io io_pp_data[3] A7	21	P12
set_io io_pp_data[4] A6	19	P11
set_io io_pp_data[5] C7	16	P9
set_io io_pp_data[6] C6	15	N11
set_io io_pp_data[7] D6	12	T11
set_io i_pp_clk C10	40	T1
WiringPi 0 is 17
schematic name	connector pin #	fpga pin #
# GPIO0/BCM17	PIN 11	M10/T13	CDONE	pg6	CAT_schematic.pdf
# GPIO1/BCM18	PIN 12	T11
# GPIO2/BCM22	PIN 15	N11	C_RESET_B
# GPIO3/BCM23	PIN 16	P9
# GPIO10/BCM10	MOSI	PIN 19	P11
# GPIO9/BCM9	MISO	PIN 21	P12
# GPIO7/BCM7	PIN	26	T7
# GPIO19/BCM19	PIN 35	T3
# GPIO16/BCM16	PCM_0	PIN 36	R4
# /BCM20	MOSI	PIN 38	R3
# /BCM21	PIN 40	T1

FPGA pin N11 BCM 22 pin 15 io_pp_data[6] C6 on icoboard needs a new pin on Rpi since it is connected on CRESET_B

FPGA pin C6 DIPSW1 io_pp_data[6] needs a pin on Rpi BCM24 T9 pin

icepll -i 100 -o 66 -f pll_para.v

F_PLLIN: 100.000 MHz (given)
F_PLLOUT: 66.000 MHz (requested)
F_PLLOUT: 65.972 MHz (achieved)

FEEDBACK: SIMPLE
F_PFD: 11.111 MHz
F_VCO: 1055.556 MHz

DIVR: 8 (4'b1000)
DIVF: 94 (7'b1011110)
DIVQ: 4 (3'b100)

FILTER_RANGE: 1 (3'b001)

PLL configuration written to: pll_para.v

sb_pll40_pad.v
 module top(
input PACKAGEPIN,
output PLLOUTCORE,
output PLLOUTGLOBAL,
input EXTFEEDBACK,
input [7:0] DYNAMICDELAY,
output LOCK,
input BYPASS,
input RESETB,
input LATCHINPUTVALUE,

//Test Pins
output SDO,
input SDI,
input SCLK
);
SB_PLL40_PAD #(
.FEEDBACK_PATH("DELAY"),
// .FEEDBACK_PATH("SIMPLE"),
// .FEEDBACK_PATH("PHASE_AND_DELAY"),
// .FEEDBACK_PATH("EXTERNAL"),

.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
// .DELAY_ADJUSTMENT_MODE_FEEDBACK("DYNAMIC"),

.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
// .DELAY_ADJUSTMENT_MODE_RELATIVE("DYNAMIC"),

.PLLOUT_SELECT("GENCLK"),
// .PLLOUT_SELECT("GENCLK_HALF"),
// .PLLOUT_SELECT("SHIFTREG_90deg"),
// .PLLOUT_SELECT("SHIFTREG_0deg"),

.SHIFTREG_DIV_MODE(1'b0),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0000),
.DIVF(7'b0000000),
.DIVQ(3'b001),
.FILTER_RANGE(3'b000),
.ENABLE_ICEGATE(1'b0),
.TEST_MODE(1'b0)
) uut (
.PACKAGEPIN (PACKAGEPIN ),
.PLLOUTCORE (PLLOUTCORE ),
.PLLOUTGLOBAL (PLLOUTGLOBAL ),
.EXTFEEDBACK (EXTFEEDBACK ),
.DYNAMICDELAY (DYNAMICDELAY ),
.LOCK (LOCK ),
.BYPASS (BYPASS ),
.RESETB (RESETB ),
.LATCHINPUTVALUE(LATCHINPUTVALUE),
.SDO (SDO ),
.SDI (SDI ),
.SCLK (SCLK )
);
endmodule

BCM4	GPCLk0	PIN 16	R9

Trying to chg set_io i_clk R9	# 100 MHz clock
fatal error: bad constraint on 'i_clk': no PLL at pin C8

Trying to chg set_io io_pp_data[6] C6
fatal error: unknown pin `N11' on package `ct256'
diff --git a/wbuart32/pptest/speechpp.pcf b/wbuart32/pptest/speechpp.pcf
index 985962a..9333a95 100644
--- a/wbuart32/pptest/speechpp.pcf
+++ b/wbuart32/pptest/speechpp.pcf
@@ -1,16 +1,16 @@
 set_io i_clk R9	# 100 MHz clock
-set_io o_ledg[0] C8
-set_io o_ledg[1] F7
-set_io o_ledr K9
+set_io o_ledg[0] A9	#icoboard C8 mapped to Catboard used make speechpp to test
+set_io o_ledg[1] B8	#icoboard F7 mapped to Catboard used make speechpp to test
+set_io o_ledr B7	#icoboard K9 mapped to Catboard used make speechpp to test

-set_io i_pp_dir C9	IOT_191
-set_io i_pp_clk C10	IOT_185 Check out i_pp_clk inside pport.v, 'cause that's the other end of that signal.
-set_io io_pp_data[0] D9
-set_io io_pp_data[1] D7
-set_io io_pp_data[2] D4
-set_io io_pp_data[3] A7
-set_io io_pp_data[4] A6
-set_io io_pp_data[5] C7

+set_io i_pp_dir R3	#icoboard C9 mapped to Catboard used make speechpp to test
+set_io i_pp_clk T1	#icoboard C10 mapped to Catboard used make speechpp to test
+set_io io_pp_data[0] R4	#icoboard D9 mapped to Catboard used make speechpp to test
+set_io io_pp_data[1] T3	#icoboard D7 mapped to Catboard used make speechpp to test
+set_io io_pp_data[2] T7	#icoboard D4 mapped to Catboard used make speechpp to test
+set_io io_pp_data[3] P12	#icoboard A7 mapped to Catboard used make speechpp to test
+set_io io_pp_data[4] P11	#icoboard A6 mapped to Catboard used make speechpp to test
+set_io io_pp_data[5] P9	#icoboard C7 mapped to Catboard used make speechpp to test
 set_io io_pp_data[6] C6
-set_io io_pp_data[7] D6
-set_io o_pp_clkfb D5 # set_io io_pp_data[8] D5
+set_io io_pp_data[7] T11	#icoboard D6 mapped to Catboard used make speechpp to test
+set_io o_pp_clkfb T13	#icoboard D5 # set_io io_pp_data[8] D5 mapped to Catboard used make speechpp to test

cd uart_rxtx/wbuart32/pptest/
sudo ~/catboard_yosys/config_cat ../basic/clktest.bin
sudo ~/catboard_yosys/config_cat speechpp.bin

cd icozip/sw/host/
./arm-wbregs -n localhost -p 8363 VERISON
Connect Failed Err: Connection refused

./arm-netpport
Listening on port 8363
Listening on port 8364

cd icozip/sw/host/
./arm-wbregs -n localhost -p 8363 VERISON
Unknown register: VERISON

cd icozip/sw/host/
on pi3-2
./arm-wbregs -n pi2-2 -p 8363 VERISON
Unknown register: VERISON