Speechpp
05/15/18

In the speechpp.pcf set_io i_clk R9. Pin R9 on the icoboard ICE_CLK is connected to IOB_81_GBIN5 on the right side of the image below.

Trying to chg set_io i_clk R9	# 100 MHz clock
To C8 USER_CLK was causing the following error
fatal error: bad constraint on 'i_clk': no PLL at pin C8

Post on #yosys
Pin C8 is my USER_CLK comes from a 100MHz osc. It is connected to IOT_197_GBIN1 on HX8K. When I try using it for as an input to PLL I get the fatal error: bad constraint on `i_clk': no PLL at pin C8.
Can only certain pins be used as inputs to PLL?
daveshah
develonepi3: use the SB_PLL40_CORE instead of SB_PLL40_PAD variant (and REFERENCECLK in instead of PACKAGEPIN)
on the left side of the image below.

ICOBOARD RPI

CATBOARD RPI

make speechpp
write_txt speechpp.asc...
icetime -d hx8k -c 75 speechpp.asc
// Reading input .asc file..
// Reading 8k chipdb file..
// Creating timing netlist..
// Timing estimate: 10.21 ns (97.91 MHz)
// Checking 13.33 ns (75.00 MHz) clock constraint: PASSED.
icepack speechpp.asc speechpp.bin
rm speechpp.asc

verilator -Wall -I../pport/ --cc speechpp.v
cd obj_dir/
make -f Vspeechpp.mk

R9 on the icoboard ICE_CLK IOB_81_GBIN5 which RPI_ICE_CLK pin 7 GPIO 4 on RPi.
On the catboard BCM4_GPCLK0 IOB_81_GBIN5
netpport.cpp

// RPi GPIO #, connector pin #, schematic name, fpga pin #
//
# define RASPI_D8 0 // PIN 11, GPIO.0, IO219, D5
# define RASPI_D7 1 // PIN 12, GPIO.1, IO212, D6
# define RASPI_D6 3 // PIN 15, GPIO.3, IO209, C6
# define RASPI_D5 4 // PIN 16, GPIO.4, IO206, C7
# define RASPI_D4 12 // PIN 19, MOSI, RPI_SPI_MOSI,A6
# define RASPI_D3 13 // PIN 21, MISO, RPI_SPI_MISO,A7
# define RASPI_D2 11 // PIN 26, CE1, IO224, D4
# define RASPI_D1 24 // PIN 35, GPIO.24, IO210, D7
# define RASPI_D0 27 // PIN 36, GPIO.27, IO193, D9
# define RASPI_DIR 28 // PIN 38, GPIO.28, IO191, C9
# define RASPI_CLK 29 // PIN 40, GPIO.29, IO185, C10
set_io io_pp_data[0] D9	36	R4
set_io io_pp_data[1] D7	35	T3
set_io io_pp_data[2] D4	26	T7
set_io io_pp_data[3] A7	21	P12
set_io io_pp_data[4] A6	19	P11
set_io io_pp_data[5] C7	16	P9
set_io io_pp_data[6] C6	15	N11
set_io io_pp_data[7] D6	12	T11
set_io i_pp_clk C10	40	T1
WiringPi 0 is 17
schematic name	connector pin #	fpga pin #
# GPIO0/BCM17	PIN 11	M10/T13	CDONE	pg6	CAT_schematic.pdf
# GPIO1/BCM18	PIN 12	T11
# GPIO2/BCM22	PIN 15	N11	C_RESET_B
# GPIO3/BCM23	PIN 16	P9
# GPIO10/BCM10	MOSI	PIN 19	P11
# GPIO9/BCM9	MISO	PIN 21	P12
# GPIO7/BCM7	PIN	26	T7
# GPIO19/BCM19	PIN 35	T3
# GPIO16/BCM16	PCM_0	PIN 36	R4
# /BCM20	MOSI	PIN 38	R3
# /BCM21	PIN 40	T1

On the catboard, FPGA pin N11 BCM 22 pin 15, is connected to CRESET_B. On the icoboard io_pp_data[6] C6	15

FPGA pin C6 DIPSW1 io_pp_data[6] needs a pin on Rpi BCM24 T9 pin

added to clktest.v input wire io_pp_data;
from speechpp.v inout wire [7:0] io_pp_data;
modified assign	o_ledr = 1'b0;--> assign o_ledr = (io_pp_data) ? 1'b1 : 1'b0;

diff clktest.v clktest_d0.v
42c42
< module	clktest(i_clk, o_ledg, o_ledr);
---
> module	clktest(i_clk, o_ledg, o_ledr,io_pp_data);
46c46
<
---
>	input wire io_pp_data;
107c107,110
<	assign	o_ledr = 1'b0;
---
>	//assign	o_ledr = 1'b0;
>	assign o_ledr = (io_pp_data) ? 1'b1 : 1'b0;
>
>

Testing 1 pin at time
testing d0-d8 then i_pp_dir & i_pp_clk

make clktest_d0
sudo ~/catboard_yosys/config_cat clktest_d0.bin
gcc -Wall -o blink blink.c -lwiringPi
sudo ./blink

~/uart_rxtx/wbuart32/basic/clktest_d0.pcf
set_io i_clk C8	# 25MHz clock ?
set_io o_ledg[0] A9 #C8
set_io o_ledg[1] B8 #F7
set_io o_ledr B7 #K9
#testing d0-d8
#set_io io_pp_data R4	#icoboard D9 mapped to Catboard used make speechpp to test
#set_io io_pp_data T3	#icoboard D9 mapped to Catboard used make speechpp to test
#set_io io_pp_data T13	#icoboard D4 mapped to Catboard used make speechpp to test
#set_io io_pp_data T6	#icoboard A7 mapped to Catboard used make speechpp to test
#set_io io_pp_data T5	#icoboard A6 mapped to Catboard used make speechpp to test
#set_io io_pp_data P9	#icoboard C7 mapped to Catboard used make speechpp to test
#set_io io_pp_data T9	#icoboard C6 mapped to Catboard used make speechpp to test
#set_io io_pp_data T11	#icoboard D6 mapped to Catboard used make speechpp to test
#set_io io_pp_data T7	#icoboard D5 # set_io io_pp_data[8] D5 mapped to Catboard used make speechpp to test

#testing i_pp_dir & i_pp_clk
#set_io i_pp_dir R3	#icoboard C9 mapped to Catboard used make speechpp to test
#set_io i_pp_clk T8	#icoboard C10 mapped to Catboard used make speechpp to test
#set_io io_pp_data R3	#icoboard C9 mapped to Catboard used make speechpp to test
set_io io_pp_data T8	#icoboard C10 mapped to Catboard used make speechpp to test

#include <wiringPi.h>
//gcc -Wall -o blink blink.c -lwiringPi
//sudo ./blink
~/uart_rxtx/wbuart32/basic/blink.c
# define RASPI_DIR 28 //BCM20	PIN 38, GPIO.28 IOB_59 R3
# define RASPI_CLK 10 //BCM8	PIN 24, GPIO.10, IOB_75	T8

# define RASPI_D0 27 //BCM16	PIN 36, GPIO.27, IOB_63	R4
# define RASPI_D1 24 //BCM19	PIN 35, GPIO.24, IOB_61	T3
# define RASPI_D2 0 //BCM17	PIN 11, GPIO.0 ,IOB_94	T13

# define RASPI_D3 21 //BCM5 PIN 29,GPIO.21 ,IOB_73	T6

# define RASPI_D4 22 //BCM6 PIN 31,GPIO.22 ,IOB_69	T5
# define RASPI_D5 4 //BCM23	PIN 16,GPIO.4, IOB_83	P9

# define RASPI_D6 5 //BCM24	PIN 18, GPIO.5, IOB_79	T9
# define RASPI_D7 1 //BCM18	pin 12, GPIO.1, IOB_89	T11
# define RASPI_D8 11 //BCM7	PIN 26, GPIO.11, IOB_75	T7
int main (void)
{
  wiringPiSetup () ;
  pinMode (RASPI_CLK, OUTPUT) ;
  for (;;)
  {
    digitalWrite (RASPI_CLK, HIGH) ; delay (500) ;
    digitalWrite (RASPI_CLK, LOW) ; delay (500) ;
  }
  return 0 ;
}

Testing 1 pin at time
testing d0-d8 then i_pp_dir & i_pp_clk
Added to clktest_out_d0.v
output wire io_pp_data;
assign	io_pp_data = (ctr[31:30] == 2'b00);

gcc -Wall -o rd_bit rd_bit.c -lwiringPi
sudo ./rd_bit
make clktest_out_d0
sudo ~/catboard_yosys/config_cat clktest_out_d0.bin
pin being rd 1 repeats several times
pin being rd 0 repeats several times
clktest_out_do.v

////////////////////////////////////////////////////////////////////////////////
//
// Filename:	clktest.v
//
// Project:	ICO Zip, iCE40 ZipCPU demonsrtation project
//
// Purpose:	To determine the actual clock rate of the ICO board. If the
//	clock is configured properly within here, then one LED will
//	flash once per second, and a second LED will flash once per minute.
//	You should be able to use your stopwatch thus with this program to
//	achieve some level of calibration.
//
// Creator:	Dan Gisselquist, Ph.D.
//	Gisselquist Technology, LLC
//
////////////////////////////////////////////////////////////////////////////////
//
// Copyright (C) 2015-2017, Gisselquist Technology, LLC
//
// This program is free software (firmware): you can redistribute it and/or
// modify it under the terms of the GNU General Public License as published
// by the Free Software Foundation, either version 3 of the License, or (at
// your option) any later version.
//
// This program is distributed in the hope that it will be useful, but WITHOUT
// ANY WARRANTY; without even the implied warranty of MERCHANTIBILITY or
// FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License
// for more details.
//
// You should have received a copy of the GNU General Public License along
// with this program. (It's in the $(ROOT)/doc directory. Run make with no
// target there if the PDF file isn't present.) If not, see
// <http://www.gnu.org/licenses/> for a copy.
//
// License:	GPL, v3, as defined and found on www.gnu.org,
//	http://www.gnu.org/licenses/gpl.html
//
//
////////////////////////////////////////////////////////////////////////////////
//
//
module	clktest(i_clk, o_ledg, o_ledr,io_pp_data);
input	i_clk;
output	wire	[1:0]	o_ledg;	// The two green LEDs
output	wire	o_ledr;	// The one red LED
output wire io_pp_data;
// Our first task is to generate a strobe that will be true at the
// top of any second. We do this using a 32-bit counter, but step
// the counter by 2^32/clock_rate. Hence, after clock_rate clocks tick
// by, the counter should roll over.
reg	pps;
reg [31:0]	ctr;
initial ctr = 0;

wire	clk_66mhz, pll_locked;
SB_PLL40_CORE #(
.FEEDBACK_PATH("SIMPLE"),
.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
.PLLOUT_SELECT("GENCLK"),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'd8),	// Divide by (DIVR+1)
.DIVQ(3'd4),	// Divide by 2^(DIVQ)
.DIVF(7'd94),	// Multiply by (DIVF+1)
.FILTER_RANGE(3'b001)
) plli (
.REFERENCECLK (i_clk ),
.PLLOUTCORE (clk_66mhz ),
.LOCK (pll_locked ),
.BYPASS (1'b0 ),
.RESETB (1'b1 )
);

assign	s_clk = clk_66mhz;

always @(posedge s_clk)
{pps, ctr} <= ctr + 32'd65;	// Valid if CLKRATE = 66MHz
//{pps, ctr} <= ctr + 32'd43;	// Valid if CLKRATE = 100MHz
// {pps, ctr} <= ctr + 32'd89; // Good if CLKRATE = 48MHz
// {pps, ctr} <= ctr + 32'd172; // Good if CLKRATE = 25MHz

// Let's set an LED to reflect this once per second value, but also
// set it so that it is true for 1/4 of a second, turning on at the
// top of the second we are referencing.
assign	o_ledg[0] = (ctr[31:30] == 2'b00);
assign	io_pp_data = (ctr[31:30] == 2'b00);
// Now, we move on to minutes. We'll count up to 60, and then restart.
// Well, in actuality, though, our counter will go from 0..59 and then
// go back to zero--so it will never actually hit 60.
reg	[5:0]	secs;
initial	mins = 6'h0;
always @(posedge s_clk)
if (secs >= 6'd60)
secs <= 6'h0;
else if ((pps)&&(secs == 6'd59))
secs <= 0;
else if (pps)
secs <= secs + 1'b1;

// We'll set the second green LED to blink when this second counter
// is at the top of a minute. We'll leave it on for a full second,
// and then off for the rest of the minute.
assign	o_ledg[1] = (secs == 6'h00);

// As for the third LED, the red one, we'll keep that one off.
assign	o_ledr = 1'b0;

endmodule

clktest_out_d0.pcf

set_io i_clk C8	# 25MHz clock ?
set_io o_ledg[0] A9 #C8
set_io o_ledg[1] B8 #F7
set_io o_ledr B7 #K9
#testing d0-d8
#set_io io_pp_data R4	#icoboard D9 mapped to Catboard used make speechpp to test
#set_io io_pp_data T3	#icoboard D9 mapped to Catboard used make speechpp to test
#set_io io_pp_data T13	#icoboard D4 mapped to Catboard used make speechpp to test
#set_io io_pp_data T6	#icoboard A7 mapped to Catboard used make speechpp to test
#set_io io_pp_data T5	#icoboard A6 mapped to Catboard used make speechpp to test
#set_io io_pp_data P9	#icoboard C7 mapped to Catboard used make speechpp to test
#set_io io_pp_data T9	#icoboard C6 mapped to Catboard used make speechpp to test
#set_io io_pp_data T11	#icoboard D6 mapped to Catboard used make speechpp to test
#set_io io_pp_data T7	#icoboard D5 # set_io io_pp_data[8] D5 mapped to Catboard used make speechpp to test

#testing i_pp_dir & i_pp_clk
#set_io i_pp_dir R3	#icoboard C9 mapped to Catboard used make speechpp to test
#set_io i_pp_clk T8	#icoboard C10 mapped to Catboard used make speechpp to test
#set_io io_pp_data R3	#icoboard C9 mapped to Catboard used make speechpp to test
set_io io_pp_data T8	#icoboard C10 mapped to Catboard used make speechpp to test

rd_bit.c

#include <wiringPi.h>
#include <stdio.h>

//gcc -Wall -o rd_bit rd_bit.c -lwiringPi
//sudo ./blink

# define RASPI_DIR 28 //BCM20	PIN 38, GPIO.28 IOB_59 R3
# define RASPI_CLK 10 //BCM8	PIN 24, GPIO.10, IOB_75	T8

# define RASPI_D0 27 //BCM16	PIN 36, GPIO.27, IOB_63	R4
# define RASPI_D1 24 //BCM19	PIN 35, GPIO.24, IOB_61	T3
# define RASPI_D2 0 //BCM17	PIN 11, GPIO.0 ,IOB_94	T13

# define RASPI_D3 21 //BCM5 PIN 29,GPIO.21 ,IOB_73	T6

# define RASPI_D4 22 //BCM6 PIN 31,GPIO.22 ,IOB_69	T5
# define RASPI_D5 4 //BCM23	PIN 16,GPIO.4, IOB_83	P9

# define RASPI_D6 5 //BCM24	PIN 18, GPIO.5, IOB_79	T9
# define RASPI_D7 1 //BCM18	pin 12, GPIO.1, IOB_89	T11
# define RASPI_D8 11 //BCM7	PIN 26, GPIO.11, IOB_75	T7
int main (void)
{
  wiringPiSetup () ;
  pinMode (RASPI_CLK, INPUT) ;
  for (;;)
  {

    printf("pin being rd %d \n", digitalRead(RASPI_CLK));
  }
  return 0 ;
}

icepll -i 100 -o 66 -f pll_para.v

F_PLLIN: 100.000 MHz (given)
F_PLLOUT: 66.000 MHz (requested)
F_PLLOUT: 65.972 MHz (achieved)

FEEDBACK: SIMPLE
F_PFD: 11.111 MHz
F_VCO: 1055.556 MHz

DIVR: 8 (4'b1000)
DIVF: 94 (7'b1011110)
DIVQ: 4 (3'b100)

FILTER_RANGE: 1 (3'b001)

PLL configuration written to: pll_para.v

sb_pll40_pad.v
 module top(
input PACKAGEPIN,
output PLLOUTCORE,
output PLLOUTGLOBAL,
input EXTFEEDBACK,
input [7:0] DYNAMICDELAY,
output LOCK,
input BYPASS,
input RESETB,
input LATCHINPUTVALUE,

//Test Pins
output SDO,
input SDI,
input SCLK
);
SB_PLL40_PAD #(
.FEEDBACK_PATH("DELAY"),
// .FEEDBACK_PATH("SIMPLE"),
// .FEEDBACK_PATH("PHASE_AND_DELAY"),
// .FEEDBACK_PATH("EXTERNAL"),

.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
// .DELAY_ADJUSTMENT_MODE_FEEDBACK("DYNAMIC"),

.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
// .DELAY_ADJUSTMENT_MODE_RELATIVE("DYNAMIC"),

.PLLOUT_SELECT("GENCLK"),
// .PLLOUT_SELECT("GENCLK_HALF"),
// .PLLOUT_SELECT("SHIFTREG_90deg"),
// .PLLOUT_SELECT("SHIFTREG_0deg"),

.SHIFTREG_DIV_MODE(1'b0),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0000),
.DIVF(7'b0000000),
.DIVQ(3'b001),
.FILTER_RANGE(3'b000),
.ENABLE_ICEGATE(1'b0),
.TEST_MODE(1'b0)
) uut (
.PACKAGEPIN (PACKAGEPIN ),
.PLLOUTCORE (PLLOUTCORE ),
.PLLOUTGLOBALaa7cfd685ce7 (PLLOUTGLOBAL ),
.EXTFEEDBACK (EXTFEEDBACK ),
.DYNAMICDELAY (DYNAMICDELAY ),
.LOCK (LOCK ),
.BYPASS (BYPASS ),
.RESETB (RESETB ),
.LATCHINPUTVALUE(LATCHINPUTVALUE),
.SDO (SDO ),
.SDI (SDI ),
.SCLK (SCLK )
);
endmodule

BCM4	GPCLk0	PIN 16	R9

Trying to chg set_io io_pp_data[6] C6
fatal error: unknown pin `N11' on package `ct256'
diff --git a/wbuart32/pptest/speechpp.pcf b/wbuart32/pptest/speechpp.pcf
index 985962a..9333a95 100644
--- a/wbuart32/pptest/speechpp.pcf
+++ b/wbuart32/pptest/speechpp.pcf
@@ -1,16 +1,16 @@
 set_io i_clk R9	# 100 MHz clock
-set_io o_ledg[0] C8
-set_io o_ledg[1] F7
-set_io o_ledr K9
+set_io o_ledg[0] A9	#icoboard C8 mapped to Catboard used make speechpp to test
+set_io o_ledg[1] B8	#icoboard F7 mapped to Catboard used make speechpp to test
+set_io o_ledr B7	#icoboard K9 mapped to Catboard used make speechpp to test

-set_io i_pp_dir C9	IOT_191
-set_io i_pp_clk C10	IOT_185 Check out i_pp_clk inside pport.v, 'cause that's the other end of that signal.
-set_io io_pp_data[0] D9
-set_io io_pp_data[1] D7
-set_io io_pp_data[2] D4
-set_io io_pp_data[3] A7
-set_io io_pp_data[4] A6
-set_io io_pp_data[5] C7

+set_io i_pp_dir R3	#icoboard C9 mapped to Catboard used make speechpp to test
+set_io i_pp_clk T1	#icoboard C10 mapped to Catboard used make speechpp to test
+set_io io_pp_data[0] R4	#icoboard D9 mapped to Catboard used make speechpp to test
+set_io io_pp_data[1] T3	#icoboard D7 mapped to Catboard used make speechpp to test
+set_io io_pp_data[2] T7	#icoboard D4 mapped to Catboard used make speechpp to test
+set_io io_pp_data[3] P12	#icoboard A7 mapped to Catboard used make speechpp to test
+set_io io_pp_data[4] P11	#icoboard A6 mapped to Catboard used make speechpp to test
+set_io io_pp_data[5] P9	#icoboard C7 mapped to Catboard used make speechpp to test
 set_io io_pp_data[6] C6
-set_io io_pp_data[7] D6
-set_io o_pp_clkfb D5 # set_io io_pp_data[8] D5
+set_io io_pp_data[7] T11	#icoboard D6 mapped to Catboard used make speechpp to test
+set_io o_pp_clkfb T13	#icoboard D5 # set_io io_pp_data[8] D5 mapped to Catboard used make speechpp to test

cd uart_rxtx/wbuart32/pptest/
sudo ~/catboard_yosys/config_cat ../basic/clktest.bin
sudo ~/catboard_yosys/config_cat speechpp.bin

cd icozip/sw/host/
./arm-wbregs -n localhost -p 8363 VERISON
Connect Failed Err: Connection refused

./arm-netpport
Listening on port 8363
Listening on port 8364

cd icozip/sw/host/
./arm-wbregs -n localhost -p 8363 VERISON
Unknown register: VERISON

cd icozip/sw/host/
on pi3-2
./arm-wbregs -n pi2-2 -p 8363 VERISON
Unknown register: VERISON