********DRAFT********
Testing MyHDL created uart_tx.v & uart_rx.v
for the CATBOARD

based UART_RX.v & UART_TX.v
04/26/18
********DRAFT********

Thu Apr 19 2018

Initial code was download from
https://www.edaplayground.com/x/Pgf
http://www.nandland.com
Command to create testuart from UART_TB.v UART_RX.v UART_TB/v includes UART_TX.v

iverilog -o testuart UART_TB.v UART_RX.v

vvp testuart
VCD info: dumpfile dump.vcd opened for output.
Test Passed - Correct Byte Received

This code was created

  // Testbench uses a 25 MHz clock
  // Want to interface to 115200 baud UART
  // 25000000 / 115200 = 217 Clocks Per Bit.
  parameter c_CLOCK_PERIOD_NS = 40;

Note the clock period of 40 nsec the time between the white marker and red marker.

Both the UART_TX and UART_RX are a case statement
IDLE, TX_START_BIT, TX_DATA_BITS, TX_STOP_BIT, and C:EANUP.
IDLE, RX_START_BIT, RX_DATA_BITS, RX_STOP_BIT, and C:EANUP.
In MyHDL the case statement was written for uart_tx.
if(r_SM_Main==IDLE):
.
.
elif (r_SM_Main==TX_START_BIT):
.
.
elif (r_SM_Main==TX_DATA_BITS):
.
.
elif (r_SM_Main==TX_STOP_BIT):
.
.
else:
.
.
and the uart_rx was similar
if(r_SM_Main==IDLE):
.
.
elif (r_SM_Main==RX_START_BIT):
.
.
elif (r_SM_Main==RX_DATA_BITS):
.
.
elif (r_SM_Main==RX_STOP_BIT):
.
.
else:
.
.

In the simulation the r_TX_BYTE is set to byte to be transmitted and a 1 clock wide r_TX_DV.
      r_TX_DV <= 1'b1;
      r_TX_Byte <= 8'h3A;
      @(posedge r_Clock);
      r_TX_DV <= 1'b0;

  Testing at 100 MHz appears okay
    Using MyHDL to create uart_rx.v with uart_rx.py
    & uart_tx.v with uart_tx.py

iverilog -o testuart tb_dut_uart_txrx.v uart_rx.v

vvp testuart
    VCD info: dumpfile dump.vcd opened for output.
    Test Passed - Correct Byte Received

Serveral simulation were tested 0x3F, 0x32, 0x38, 0x3A, 0x41.
 3F transmitted & recived

00111111
32 transmitted & recived
00110010

38 transmitted & recived

00111000
3A transmitted & recived

00111010
41 transmitted & recived

0100001